## Slide 1
Pepper Programming
Dr. Samuele Vinanzi
Robotics and Artificial Intelligence
Sheffield Hallam University

## Slide 2: SOFTBANK PEPPER ROBOT
Manufactured in 2014 by SoftBank (formerly Aldebaran), a Japanese company.
«Pepper is intended to make people enjoy life, enhance people's lives, facilitate relationships, entertain and connect people with the outside world»
PROCESSOR | Atom E3845
CPU | Quad core
Clock speed | 1.91 GHz
RAM | 4 GB DDR3
GPU | Intel HD graphics 792 MHz

## Slide 3: SOFTBANK PEPPER ROBOT
Tactile sensors
Microphones
Depth cameras
Speakers
Tablet
Sonars
RGB cameras
Gyroscope
Inertial sensors
Tactile sensors
Lasers
Bumpers
Omnidirectional wheels

## Slide 4: SOFTBANK PEPPER ROBOT
3D rotational axes (roll, pitch yaw)

## Slide 5: Middleware: naoqi
Proprietary software of SoftBank Robotics.
Used across their robots: Nao and Pepper.
Interfaces in Python and C++.

## Slide 6: PROGRAMMING PEPPER
ROS
Choregraphe
Python C++

## Slide 7: CHoregraphe
Easiest way of programming the robot.
No code: only graphical blocks that are combined to form behaviors.
Useful for:
  Learning robot programming
  Developing simple behaviors
  Simulation
  Monitoring the robot
  Designing animations
  http://doc.aldebaran.com/2-5/software/choregraphe/tutos/index.html

## Slide 8: Choregraphe OVERVIEW

## Slide 9: CHOREGRAPHE OVERVIEW

## Slide 10: PYTHON PROGRAMMING
NAOqi is the name of the main software that runs on the robot and controls it.
Interfaces in Python and C++.
http://doc.aldebaran.com/2-5/dev/naoqi/index.html

## Slide 11: PYTHON programming

## Slide 12: PYTHON PROGRAMMING
from naoqi import ALProxy
IP = "pepper.local"
PORT = 9559
tts = ALProxy("ALTextToSpeech", IP, PORT)
tts.setLanguage("English")
tts.say("Hello, world!")
Hello, world!

## Slide 13: PYTHON PROGRAMMING
from naoqi import ALProxy
IP = "pepper.local"
PORT = 9559
motion = ALProxy("ALMotion", IP, PORT)
tts = ALProxy("ALTextToSpeech", IP, PORT)
motion.moveInit()
id = motion.post.moveTo(0.5, 0, 0) # (x; y; theta)
motion.wait(id, 0)
tts.say("I have walked")
from naoqi import ALProxy
IP = "pepper.local"
PORT = 9559
motion = ALProxy("ALMotion", IP, PORT)
tts = ALProxy("ALTextToSpeech", IP, PORT)
motion.moveInit()
motion.moveTo(0.5, 0, 0) # (x; y; theta)
tts.say("I am walking")
Talks after walking
Talks while walking

## Slide 14: Python programming
ALVideoDevice
ALTextToSpeech
ALAnimatedSpeech
ALMotion
ALFaceTracker
ALLeds
ALLandmarkDetection
ALMemory
ALSpeechRecognition
Useful modules to keep in mind (check documentation for full API description):
API documentation: http://doc.aldebaran.com/2-5/naoqi/index.html